## Slide 1: PCB Business Card (SP)
SP Digital Tech Talk (18 May 2017)
Hackware v1.5 (24 Feb 2016)
By: Yeo Kheng Meng (yeokm1@gmail.com)
https://github.com/yeokm1/pcb-name-card-sp

## Slide 2: Backstory June 2015
The spelling mistake

## Slide 3: Typical business cards

## Slide 4: Existing PCB business cards
Logic gates: http://willfj.com/pcb-business-card/
USB keyboard entry: http://eleccelerator.com/usb-business-card/
Light ring: http://www.limpkin.fr/index.php?post/2014/06/16/My-business-card-v2
Flash Drive emulation: http://makezine.com/2012/08/22/pcb-business-card-2/

## Slide 5: Goals of my business card
Be different
Be useful
Appear classy but not too expensive

## Slide 6: My previous name cards

## Slide 7: Feature goals
2 versions
  Thin low cost
  Thick high cost
Surface-mounted components
  White LED
  Ultraviolet LED
  Slide Switches
Quick adding of my contact
  QR code
  Near Field Communication (NFC)
Ruler

## Slide 8: White LED (torch)
Avago Neutral White
PLCC-2 package (3.2 x 2.8 x 1.9mm)
Add 330 ohm resistor to ↓ current
  1mA current

## Slide 9: Ultraviolet LED
Vishay
PLCC-2 package (3.2 x 2.8 x 1.9mm)
405nm (near-UV)
Current usage ~3mA

## Slide 10: UV LED in action

## Slide 11: Switches
C&K Components DPDT Minature slide switch
3mm height

## Slide 12: Why 2 batteries?
Coin cells connected in parallel to reduce current load
High currents reduce overall battery capacity
Two batteries results in >2x single battery life
Weight balance
Source:
Nordic Semiconductor, Sept 2011: High pulse drain impact on CR2032 coin cell battery capacity
http://m.eet.com/media/1121454/c0924post.pdf

## Slide 13: Quick contact adding 1: QR Code
QR code contains vCard
  BEGIN:VCARD
  VERSION:3.0
  N:Yeo;Kheng Meng
  TITLE:IoT Engineer
  ORG:SP Group
  EMAIL;type=INTERNET;type=WORK;:xxx@spgroup.com.sg
  EMAIL;type=INTERNET;type=PERSONAL;:xxx@gmail.com
  TEL;TYPE=WORK,VOICE:+65 0000000
  TEL;TYPE=CELL,VOICE:+65 12345678
  URL;WORK:https://www.spgroup.com.sg
  URL:http://yeokhengmeng.com
  URL:https://www.linkedin.com/in/yeokhengmeng
  END:VCARD
iOS Demo

## Slide 14: Quick contact adding 2: NFC
  NFC chip contains vCard
Thin NFC chip on thin version
  NXP NTAG216 (NT2H1611)
  0.26mm height
  HXSON-4/SOT1312-1 package (1.5mm x 2mm)
  888 bytes
  50pf input capacitance
Large NFC chip on thick version
  NXP NTAG I²C (NT3H1201)
  1.1mm height
  TSSOP-8 package (5mm x 3mm)
  1904 bytes
  50pf input capacitance
Android Demo

## Slide 15: NFC Antenna Design
PCB antenna on TOP layer
Antenna calculations
  F0: 13.56Mhz
  Ctun = Tuning capacitance
  N: Number of turns
  Dout: Outer diameter
  Din: Inner diameter
Antenna fixed values
  35um layer thickness as set by PCB manufacturer
  0.5mm width and gap to ease drawing of traces
  Aim for antenna resonance of 50pF to match NFC chip
  -> Reduce BOM of another tuning capacitor
I dislike calculations so… I used Panasonic NFC Design Navigator
  http://www.semicon.panasonic.co.jp/en/tool/nfcdesignnavigator/
Antenna calculations source:
http://www.st.com/st-web-ui/static/active/jp/resource/technical/document/application_note/CD00221490.pdf

## Slide 16: Assembly Process 1
Stencil and solder paste

## Slide 17: Assembly Process 2
Hot plate reflow soldering
Hand soldering for battery holders

## Slide 18: Cost (SGD)
Pieces | Thin | Thick
10 | $7.73 | $15.53
50 | $3.74 | $10.53

## Slide 19: Future work (Concept card)
Sensor suite
  Bosch BME280: temperature/humidity/pressure sensor
  Maxim MAX30100: Pulse Oximeter and Heart-Rate Sensor
  Silicon Labs SI1145: UV Sensor
  Texas Instruments TMP007: IR thermometer
OLED screen
Bluetooth Low Energy
  Rigado BMD-300 or Raytac MDBT42 nRF52 module
LIR2450 3.6V rechargeable coin-cell
Microchip MCP73831 battery charging IC

## Slide 20: Sensor breakouts
Maxim MAX30100 breakout
Pulse Oximeter & Heart-Rate Sensor
By MicroElektronika
Bosch BME280 breakout
Temperature & humidity
https://github.com/yeokm1/pcb-bme280-breakout
TMP007 breakout
IR Thermometer
By Adafruit
SI1145 breakout
UV Sensor
By Adafruit

## Slide 21: OLED screen
3cm x 1.5cm
128 x 64 pixels. 0.96” diagonal
Univision Technology UG-2864HSWEG01

## Slide 22: Power source
LIR2450 rechargeable cell
3.6V 120mAh
24.5mm x 5mm
LIR2450 charger
By: theledart
Based on MCP73831

## Slide 23: It's easier to ask forgiveness than it is to get permission. (Grace Hopper, 1986)
By: Yeo Kheng Meng (yeokm1@gmail.com)
https://github.com/yeokm1/pcb-name-card-sp